## Slide 1: Accessibility and the iPad
Switch Access
Voice Over
Speech Access
And More!

## Slide 2: Overview
Accessibility features in Apple products with iOS 8.4
  iPads 3 and above
  iPhone 4s and above
Settings ->General ->Accessibility
Lost?
  Tips under the buttons
Apple Accessibility

## Slide 3: Accessibility Shortcut
Very Bottom of accessibility features
DO FIRST. SELECT ALL OPTIONS
Triple clicking the home button will bring up a menu
Turn accessibility settings off or on.

## Slide 4: Speech
Speak Selection
  Option to speak selected text
Speak Screen
  2 finger swipe from top pf screen to hear content of screen
Change Voices
Highlight Context
  Like karaoke
Speak Auto Text
  Automatically speak corrected words
  CAREFUL

## Slide 5: Voice Over
Speak Hints
Use Pitch Change
Use Sound Effects
  Informs you when you switch what is on screens and such
Speech
  Change languages and dialects
  Alex
Typing Feedback
Speak Notifications
Large Cursor
Rotor
  Turn two fingers as you would a dial to open up the Rotor
  Rotor has shortcuts during voice over
Rotor Options
Rotor Visual

## Slide 6: Voice Over Braille Display
Braille display without physical keyboard (1)
Braille display with a physical keyboard
  Hook up with Bluetooth

## Slide 7: Hearing Basics
Facetime
  Signing
Subtitles and Captioning
Siri
  Speech to text on notes
Alternative Alerts
  LED Flash
  Vibrations
Hearing Aids
  Audibel, Audigy, Beltone, Cochlear, MictoTech, NuEar, ReSound, Starkey
  Bluetooth connection
  Manage hearing aid from phone

## Slide 8: Physical and Motor Skills
Siri 3rd Party Keyboard Support
Switch Access Dictation
Assistive Touch Keyboard shortcuts

## Slide 9: Basics
Siri
  When plugged into charger say “hey Siri”
  “Open Maps”
Dictation
  Tap little microphone for speech to text
Keyboards
  3rd party support
  Keyboard shortcuts LOL
  Word Prediction
Word Prediction
Keyboard Shortcuts
Siri

## Slide 10: Assistive Touch
Creature gestures of your own
On every screen
Compatible with switches
Lock device, home button, shortcuts

## Slide 11: Switch Access
First Connect your device through
  Bluetooth
  Switch interfaces
  Built in
Bluetooth
Switch interface
Built in camera
  improving
Switch Control
  Automatic or Do it yourself?
  Cursor size
  Timing
  Loops

## Slide 12: Questions?