## Slide 1: Switch Access
For Apple products

## Slide 2: Kate Moseley AT Specialist
TASC employee that contracts with STAR to provide AT webinars and trainings
http://www.startraining.org/
Power Point
kmoseley@ucphuntsville.org

## Slide 3: TASC and STAR
TASC
  Technology Assistance for Special Consumers
  AT consultations, evaluations, informational sessions, and Technical Assistance
  Lending Library check out equipment for 2-3 weeks
    Switches, mounts, adaptive toys, communication aids, aids to daily living, and computer keyboards, mice, and joystick adaptations
STAR
  Alabama’s assistive technology resource
  AT4ALL
    http://al.at4all.com
    Online database that provides current inventory of AT and medical equipment. You may also post want ads for items not listed.
    Wheelchairs, Scooters, Shower/ Bath Aids, Beside Commodes, Hospital beds, Walkers and canes, ramps and lifts, and more.

## Slide 4: Objectives
Locate Switch Access
Turn Switch Access on and off
Understand the settings of Switch Access
Blue Tooth & Adapter Switches

## Slide 5: Switches
Many switches
RJ Cooper and Ablenet
  User friendly
  Many adaptaions
Blue 2
  By Ablenet
  Bluetooth
    Wireless connection
Wired Switches
  Tapio iOS and USB Switch Interface
    Mac, iPad Air, iPad Mini, iPhone 5, iPhone 6
  Pererro
    Works directly with the iPhone or iPad
    4th generation iPhone and iPod Touch, and iPad 2
Blue 2
Pererro Switch interface
Tapio

## Slide 6: Blue Tooth
How do I set up blue tooth?
Having difficulties setting up to Bluetooth?
  Make sure Blue Tooth device is fully charged
  Turn off devices and turn it back on
  “forget” the device then connect again
    Tap the little “i” with a circle around it
Blue 2

## Slide 7: Switch Interfaces
Do not work as switches by themselves
Need an external switch to work
Once connected
  Settings -> general -> accessibility -> switch access
Set up your switch similar to the way we set up the bluetooth switch
  switches -> new switch -> external
  Make sure switch control is on and you are ready to go!

## Slide 8: Tapio Switch
Versatile Switch
  USB plug for computers
  Lightning to USB Adaptor for Apple products
Lightning to USB adapter plugs into iPad
Tapio USB plugs into lightning adapter
Switch plugs into Tapio
Switch is ready to go
+
=
Note: when I plug in Tapio my iPad Air 2 says the switch is not compatible, but it works anyways. I ignore that notification and move on through the steps.

## Slide 9: Pererro Switch
Plug in Pererro into bottom of iPad
Plug switch cable into Pererro
Switch is ready to go and functional through Switch Access!